## Slide 1: QG-Scanning with Network RTK SRS1 & SRS2 Part 1 of 3
Connecting MAGNET Flow and configuring field controllers for the SRS1 and SRS2

## Slide 2: Download MAGNET Flow
For Android, download MAGNET Flow from the Google play store.

## Slide 3: Connecting to the scanner’s Wi-Fi
Press the power button on the SRS2 or SRS1 until it lights up green to power it on.
The Power LED will flash green while powering up.
Wait until the power LED turns solid green.
Open MAGNET Flow
Tap on the SRS2 or SRS1.

## Slide 4: Connecting to the scanner’s Wi-Fi
Tap on Please set up WiFi.
Connect to the SRS2 or SRS1

## Slide 5: Connecting to the scanner’s Wi-Fi
To use the SRS2 or SRS1 for the first time, connect to the instrument’s Wi-Fi.
Access your field collector's WLAN/Wi-Fi connection settings.

## Slide 6: Establish a Wi-Fi Connection
Select the Wi-Fi network starting with SOKKIA SR S2_ (last 4 digits of SN).
Enter the Wi-Fi password: sokkiasrs2
SRS2
Select the Wi-Fi network starting with SOKKIA SR S1_ (last 4 digits of SN).
Enter the Wi-Fi password: sokkiasrs1
SRS1

## Slide 7: Connecting to the scanner’s Wi-Fi
The instrument’s Wi-Fi name will appear next to WiFi name in the MAGNET Flow app.
Tap Connect Device.

## Slide 8: Connecting to the scanner’s Wi-Fi
To operate the SRS2 with an NTRIP VRS service, the user must have the following:
Field controller/mobile device with an active internal SIM card
Field controller/mobile device onboard hotspot
NTRIP VRS service login credentials
SLAM Scanner: SRS2 or SRS1
SLAM Scanner
Field Controller
SIM CARD
TopNet
Hot Spot

## Slide 9: Configure SHC700 Settings
You can customize the settings options on the SHC700.
From the home screen, drag your finger down slowly.
Tap on the pencil icon.
Drag the menu options towards the top.
  You will need Location and & Hotspot.
When finished, tap the back arrow

## Slide 10: SHC700 or Android device
Swipe all the way down for settings.
Verify connection and active SIM card for cellular connection.
Next, swipe left to search for the hotspot settings.

## Slide 11: SHC700 or Android device
Tap and hold on Hotspot to open Hotspot settings.

## Slide 12: SHC700 or Android device
Enable Use Wi-Fi hotspot.
Input a Hotspot password that is easy to remember.
Any password works.

## Slide 13: SHC700 or Android device
Tap Hotspot Configuration Information.

## Slide 14: SHC700 or Android device
Input the Hotspot name and Hotspot Password
Tap ok.

## Slide 15: SHC700 or Android device
A pop-up window will appear, stating that the instrument has connected to the field controller’s hotspot.

## Slide 16: SHC700 or Android device
Once connected to the Wi-Fi hotspot, the device name and IP address should populate.
Next, click connect device.

## Slide 17: SHC700 or Android device
Once the device connects, the user will see a Device connected message.
A pop-up window will appear showing the status of the sensors on the SRS1/SRS2.
Tap Ok.
Read part 2 of this guide for the next steps to configure the NTRIP VRS network connection and achieve an RTK fix solution.