## Slide 1: QG-Scanning with Network RTK SRS1 & SRS2 Part 2 of 3
Configuring NTRIP on the FC-700 Android

## Slide 2: Android Settings for NTRIP VRS
Tap Start Operation.

## Slide 3: Android Settings for NTRIP VRS
To configure the NTRIP VRS settings, tap on the gear icon on the top right corner of the screen.

## Slide 4: Android Settings for NTRIP VRS
Tap on RTK Link.
If you don’t see the option for RTK link, tap the back arrow until you return to the main page.
When asked if you want to use RTK, tap Yes.

## Slide 5: Android Settings for NTRIP VRS
Input the following NTRIP VRS information:
  IP address
  Port
  Username
  Password

## Slide 6: Android Settings for NTRIP VRS
Tap on the down arrow to download the mountpoints.

## Slide 7: Android Settings for NTRIP VRS
Scroll down the mountpoint list and select RTK_MSM5.
After selecting the mountpoint, tap the enter icon on the bottom right corner of the keyboard.

## Slide 8: Android Settings for NTRIP VRS
MAGNET Flow will save the NTRIP connection details for the future.
The icon on the top right of the screen includes the previously saved NTRIP settings.
The icon to the right of the username allows the user to recall saved NTRIP logins
Tap on the Blue Submit button.

## Slide 9: Android Settings for NTRIP VRS
Make sure that the SRS2 or SRS1 has obtained an RTK Fix solution.
The green Fixed text and green satellite circle indicates that the system has an RTK fixed solution.
Tap the play icon to start data collection.