## Slide 1: QG-Scanning with Network RTK SRS1 & SRS2 Part 3 of 3
Starting a New Project and Scanning With the SHC700 Android

## Slide 2: Android Settings for NTRIP VRS
Select a project to add the acquisition to an existing project.
If this is a new project, tap New Project.

## Slide 3: Android Settings for NTRIP VRS
Input the Project name.
Under Coordinate System Settings, select Custom Selection.
Tap on Settings to select the coordinate system.

## Slide 4: Android Settings for NTRIP VRS
If the coord system is set to Automatic, MAGNET Flow will select the appropriate UTM zone in meters.

## Slide 5: Android Settings for NTRIP VRS
Tap on the magnifying glass icon and type key words such as ftUS NAD83.
To use US Feet, select the projection that has (ftUS)
The projection options without units are in Meters by default.
Select the projection from the filtered list.
Tap the check mark on the bottom right to apply changes.

## Slide 6: Android Settings for NTRIP VRS
Tap Commit to save your settings.

## Slide 7: Android Settings for NTRIP VRS
Set the SRS2 or SRS1 on a flat surface.
Note: the surface does not have to be perfectly level.
Tap on Start Collection.

## Slide 8: Android Settings for NTRIP VRS
Tap on Outdoor and select one of the environment options:
  Outdoor
  Indoor
  Indoor + Outdoor
  Tunnel
  Open Area
Next to Equipment form, select one of the options:
  Handheld
  Pole
  Vehicle (SRS1 only)
Click on Start collection.

## Slide 9: Android Settings for NTRIP VRS
Leave the CRS2 or CRS1 scan on a flat surface during the initial 30-second calibration.
The text at the top will appear as Collection preparation during the calibration.

## Slide 10: Android Settings for NTRIP VRS
After 30 seconds, the text at the top will change to Collecting and appear green.
Also, notice that the scan data starts appearing on the screen.
This indicates that the calibration is complete.
Now, pick up the scanner and start scanning.